## Slide 1
Experiment No. 1
Problem Definition: To implement MOD-4 counter on LEDs connected to Port 2 using
Software delay
Hardware delay

## Slide 2
Objectives of the Experiment:
To demonstrate the interfacing of LEDs connected to Port2 of 8051 Microcontroller.
To develop an 8051 ‘C’ code to display the MOD-4 count 00,01,10,11 on LEDs connected to Port2

## Slide 3: MOD-4 Counter Implementation
MOD-4 counter has four count states 00,01,10,11.
Two LEDs are connected to Port 2 pins 4 and 5.
To display the count 00, 01,10,11 on LEDs Port 2 is loaded with the data 0x00, 0x10,0x20, 0x30 respectively.

## Slide 4: Delay Generation using software
Delay can be generated by for loop
Example: The delay routine shown below generates 250 milliseconds of time delay(for itime=250)
void delay(unsigned int itime)
{
  unsigned int i,j;
for(i=0;i<itime;i++)
for(j=0;j<1275;j++);
}

## Slide 5: Delay Generation using Hardware
Delay can be generated by Hardware(Timer)
Example: 50ms Time delay generation using Timer 0 in Mode 1

## Slide 6: Delay Generation using Hardware
void T0M1Delay(void)
{
TMOD=0X01; //TIMER 0 MODE 1(16-BIT MODE)
TL0= 0XFE; // LOAD TL0 WITH COUNT 0FE
TH0=0X4B; // LOAD TH0 WITH COUNT 4B
TR0=1; // START TIMER
while(TF0==0); //WAIT FOR TF0 TO ROLL OVER
TR0=0; //TURN OFF T0
TF0=0; // CLEAR TF0
}

## Slide 7: INTERFACING BLOCK DIAGRAM
8051 MICROCONTROLLER
P2.4
P2.5
LED0
LED1

## Slide 8
Algorithm for the experiment
STEP 1 : INCLUDE THE HEADER FILE ‘’at89c51ed2.h’’
STEP 2 : DECLARE THE DELAY ROUTINE (CASE1: SOFTWARE DELAY,
CASE 2: HARDWARE DELAY)
STEP 3 : DECLARE VARIABLES i, j, itime
STEP 4 : BEGIN MAIN
STEP 5 : REPEAT LOOP FOREVER USING WHILE(1)
STEP 6: SEND THE VALUE 0X00, 0X10,0X20,0X30 ON P2
STEP 7: CALL DELAY BETWEEN EACH VALUE
STEP 8: END

## Slide 9
#include "at89c51ed2.h“
void delay(unsigned int);
void main(void)
{
while(1)
{
P2=0x00;
delay(250);
P2=0x10;
delay(250);
P2=0x20;
delay(250);
P2=0x30;
delay(250);
}
}

## Slide 10
//SOFTWARE DELAY GENERATION
void delay(unsigned int itime)
{
  unsigned int i,j;
for(i=0;i<itime;i++)
for(j=0;j<1275;j++);
}

## Slide 11
#include "at89c51ed2.h“
void T0M1delay(void);
void main(void)
{
while(1)
{
P2=0x00;
delay();
P2=0x10;
delay();
P2=0x20;
delay();
P2=0x30;
delay();
}
}

## Slide 12
// HARDWARE DELAY GENERATION USING TIMER 0 IN MODE1
void T0M1Delay(void)
{
TMOD=0X01; //TIMER 0 MODE 1(16-BIT MODE)
TL0= 0XFE; // LOAD TL0 WITH COUNT 0FE
TH0=0X4B; // LOAD TH0 WITH COUNT 4B
TR0=1; // START TIMER
while(TF0==0); //WAIT FOR TF0 TO ROLL OVER
TR0=0; //TURN OFF T0
TF0=0; // CLEAR TF0
}

## Slide 13: Connection Details
Port 2 to CN11 of Microcontroller Evaluation Board.

## Slide 14
Learning Outcomes of the Experiment
At the end of the session, students should be able to :
Interface LEDs connected to Port 2 of 8051 Microcontroller
Develop ‘C’ code to display the MOD-4 count 00, 01, 10, 11 on LEDs connected to 8051 Microcontroller.

## Slide 15: Inquiry based learning
Interface 8051 with the LEDs connected to PORT 2.
Develop the algorithm and 8051 Embedded ‘C’ program to implement MOD-4 DOWN counter.
Develop the algorithm and 8051 Embedded ‘C’ program to implement 2 bit UP/DOWN counter.